## Slide 1: Joaquin Salas Process Control Systems Engineering Intern

## Slide 2
About Me
Projects
  Add Seal Pot Inst. To 730-P101A/B
  RLE Compressors Cause & Effect
  Install Specific Gravity and pH Meters
  Radar Gauge TKs 109/115
  Control Valves TKs 109/115
  More Projects
Miscellaneous
Intern Experience
Closing Statement
Name
Date Presenting
Agenda

## Slide 3
Joaquin Salas
7/16/2024
About Me
Hometown - Amarillo, Texas
Texas A&M University
  B.S. Electrical Engineering
  Graduating Spring 2025
Process Control Engineer Intern
  Mentor – Jordan Byars
  Supervisor – Slater Ebeling
Interests
  Playing guitar
  Training my dog
  Running

## Slide 4
Problem Statement: No instrumentation to alert operators to potential seal problems.
Proposed Solution: Add Seal Pot Instrumentation to both IC8 Reactor Recycle Pumps to alert Operators of potential seal issues.
  Adding Pressure Transmitter and Level Switch.
  Show readings in DCS.
Name
Date Presenting
Add Seal Pot Inst. to 730-P101A/B
Seal Pot P&ID
Summary/Important Comment Tile

## Slide 5
Name
Date Presenting
Add Seal Pot Inst. to 730-P101A/B
Contribution:
  Specifying Instrumentation
  IFA/IFC
  MOC
Takeaways:
  Knowledge of Seal Pots
  Problem Statement to Completion
  MOC
Summary/Important Comment Tile

## Slide 6
Purpose:
To visually map out and document the relationships between triggers (causes) and their effects on system operations.
Takeaways:
Name
Date Presenting
RLE Compressors Cause & Effect
Summary/Important Comment Tile

## Slide 7
Moving Forward:
Name
Date Presenting
RLE Compressors Cause & Effect
Cause & Effect
Summary/Important Comment Tile

## Slide 8
Name
Date Presenting
Install Specific Gravity and pH Meters

## Slide 9
Problem Statement: Reliability issues with tanks using d/p instruments.
Proposed Solution: Replace or add to the tanks d/p cell level with alternative level instruments.
  Replace existing level gauge with radar
  Non-contact measurement
  Accuracy - not affected by density changes in process conditions.
Name
Date Presenting
Radar Gauge 910-TK109/115
Redlined P&ID
Summary/Important Comment Tile

## Slide 10
Contributions:
Found tie in point that does not require new welds
Submitted DWR
Takeaways:
Radar Level Transmitter (Vega)
Floating Roof Tanks
Name
Date Presenting
Radar Gauge 910-TK109/115
Summary/Important Comment Tile

## Slide 11
Problem Statement: Valves are not easily accessible in wet and muddy conditions.
Proposed Solution: Replace with chopper valves so the valves may be opened/closed from the control room.
  Evaluated cost-effective solutions.
  Confirm availability of instrument air.
  Coordinate with Operations, Process, and Vendors.
Takeaways: Cost Analysis, Chopper Valves
Outcome: Awaiting design package
Name
Date Presenting
Control Valves for TKs 109/115
Summary/Important Comment Tile

## Slide 12
Option 1: Ball Valve
~ $50,000 + Installation
Quarter Turn Valve
Option 2: Butterfly Valve
~ $15,000 + Installation
Quarter Turn Valve
Name
Date Presenting
Control Valves for TKs 109/115
Summary/Important Comment Tile

## Slide 13
Name
Date Presenting
Control Valves for TKs 109/115
Summary/Important Comment Tile
 | Ball Valve | Butterfly Valve
Material | Carbon Steel | Ductile Iron
Turn Radius | Quarter turn | Quarter turn
Mechanical Change Required | No | Yes
Cost | $50,000 | $15,000

## Slide 14
#2 Amine Still Feed Instrumentation
  Sulphur experts conducted an amine system evaluation.
  Recommendation to install Temperature Transmitter downstream of E-109/110/111.
    Awaiting Design Package.
Mag Tech for NC4 Contactor
  Existing sight glasses are stained, can not read level.
  Replace with Mag Tech.
    Working with Emerson on Quote.
Replace RSW LEL Monitors
  Existing LEL monitors are obsolete and down to two warehouse spares.
  Replace existing U9500 CAT BEAD detectors with Draeger Polytron 8700.
    Completed MOC and EWR Closure.
Pressure Indication 820-TK5802
  Low alarm set at 2 psig to ensure nitrogen blanket is adequate to prevent oxygen ingress.
    Received Design Package.
Name
Date Presenting
More Projects
Summary/Important Comment Tile

## Slide 15
Splicing, testing, and labeling fiber optics.
Help Jordan install and configure SEL RTAC for wind turbine farm.
Replace monitors/TV screens for operators.
Helping Matt
Working with Kaityln on Wireless pump monitoring
Name
Date Presenting
Miscellaneous
Summary/Important Comment Tile

## Slide 16
Name
Date Presenting
Intern Experience
Volunteering:
Highway Trash Pickup
Corn/Fry Booth
Meat Wrapping
Meals on Wheels
Other:
Clay Shoot
Dogie Days
Windturbine Climb
Intern Symposium
Sod Poodles Game
Dinner with Controls Group
Summary/Important Comment Tile

## Slide 17
Questions?
Name
Date Presenting
Thank You!
Go back to school at Texas A&M
2 Semesters until graduation
Available for full-time job opportunities